## Slide 1: Altitude control of Cessna Citation 500 aircraft
Crippa Davide 509769
Moroni Gianluca 503424
Mongini Paolo 507997
Bordonali Mattia 496468
Notes: NOTA:
per cambiare l'immagine in questa diapositiva, selezionarla ed eliminarla. Quindi fare clic sull'icona Immagini nel segnaposto per inserire l'immagine desiderata.

## Slide 2: Introduction
Variables
States:
: Angle of attack [rad]
𝑥_1: Angle of attack [rad]
: Pitch angle [rad]
𝑥_2: Pitch angle [rad]
: Pitch rate [rad/s]
𝑥_3: Pitch rate [rad/s]
: Altitude [m]
𝑥_4: Altitude [m]
Inputs:
: Elevator angle [rad]
𝑢: Elevator angle [rad]
Variables

## Slide 3: Introduction
Model
The model is linearized at an altitude of 5000 m and a speed of 128.2 m/sec

## Slide 4: Introduction
Constraints
Elevator angle (): rad)
Elevator angle (𝑢): ±15° (±0,262 rad)
Pitch angle (): ( rad)
Pitch angle (𝑥_2): ±20° (±0,349 rad)
Elevator slew rate: ( rad/s)
Elevator slew rate: ±30°/𝑠𝑒𝑐 (±0,524 rad/s)
Constraints
Initial States
: Angle of attack = 0°
𝑥_01: Angle of attack = 0°
: Pitch angle = 15° = 0.2618 rad
𝑥_02: Pitch angle = 15° = 0.2618 rad
: Pitch rate = 0 rad/s
𝑥_03: Pitch rate = 0 rad/s
: Altitude = -300 m
𝑥_04: Altitude = -300 m
Initial States

## Slide 5: LQ Controller
General rules for computing LQ controller
Q
R
Q
R
Aggressive action on the states
Soft action on the control
Soft action on the states
Aggressive action on the control
Notes: PUNTO 1

## Slide 6: LQ Controller: 1° attempt

## Slide 7: LQ Controller: 2° attempt

## Slide 8: LQ Controller: 3° attempt

## Slide 9: LQ Controller: 4° attempt

## Slide 10: LQ Controller Discrete Time
Shannon Theorem
𝜔_𝑠𝑎𝑚𝑝𝑙𝑖𝑛𝑔>2∗𝜔_𝑐
𝑇_𝑠𝑎𝑚𝑝𝑙𝑖𝑛𝑔=(2∗𝜋)/𝜔_𝑐 =0,0793 𝑠
𝜔_𝑠𝑎𝑚𝑝𝑙𝑖𝑛𝑔=2∗𝜋∗𝑓_𝑠𝑎𝑚𝑝𝑙𝑖𝑛𝑔=(2∗𝜋)/𝑇_𝑠𝑎𝑚𝑝𝑙𝑖𝑛𝑔
𝑓_𝑠𝑎𝑚𝑝𝑙𝑖𝑛𝑔=1/𝑇_𝑠𝑎𝑚𝑝𝑙𝑖𝑛𝑔
Shannon Theorem
Notes: PUNTO 2

## Slide 11: LQ Controller Discrete Time
Simulink Scheme: Discretized Controller (, )
Simulink Scheme: Discretized Controller (𝑄_4, 𝑅_4)

## Slide 12: LQ Controller Discrete Time
Results for Discretized Controller

## Slide 13: LQ Controller Discrete Time
Comparison between Continuous and Discrete: Pitch Angle

## Slide 14: LQ Controller Discrete Time
Comparison between Continuous and Discrete: Altitude

## Slide 15: LQ Controller Discrete Time
Comparison between Continuous and Discrete: Pitch Rate

## Slide 16: MPC Controller
General rules for computing MPC controller
MPC is based on cost minimization in horizon steps
MPC is based on cost minimization in 𝑁 horizon steps
AS not always guaranteed
For AS stability results in uncostrained case:
Boundary matrix equal to Riccati solution equation even if optimal control problem is not feasable with constraints.
Boundary matrix 𝑆 equal to Riccati solution equation 𝑃 ̅ even if optimal control problem is not feasable with constraints.
If short we cannot acheive AS
If 𝑁 short we cannot acheive AS
horizon sufficently long
𝑁 horizon sufficently long
General rules for computing MPC controller
Notes: PUNTO 3

## Slide 17: MPC Controller
MPC of linear systems in state space form
𝑀𝑜𝑑𝑒𝑙:{█(𝑥(𝑘+1)=𝐴 𝑥(𝑘)+𝐵 𝑢(𝑘)@𝑦(𝑘)=𝐶(𝑘))┤
𝐶𝑜𝑠𝑡 𝑓𝑢𝑛𝑐𝑡𝑖𝑜𝑛:𝐽(𝑥(𝑘),𝑢(.),𝑘)=∑24_(𝑖=0)^(𝑁−1)▒〖(‖𝑥(𝑘+𝑖)‖_𝑄^2+‖𝑢(𝑘+𝑖)‖_𝑅^2 )+‖𝑥(𝑘+𝑁)‖_𝑆^2 〗
𝑁→𝑃𝑟𝑒𝑑𝑖𝑐𝑡𝑖𝑜𝑛 ℎ𝑜𝑟𝑖𝑧𝑜𝑛
𝑄=𝑄^′≥0, 𝑅=𝑅^′>0,𝑆=𝑆′≥0
𝑥∈𝑅^𝑛, 𝑢∈𝑅^𝑚, 𝑦∈𝑅^𝑝
𝐶𝑜𝑛𝑡𝑟𝑜𝑙 𝑠𝑒𝑞𝑢𝑒𝑛𝑐𝑒→𝑢(𝑘), 𝑢(𝑘+1),…,𝑢(𝑘+1−𝑁)
MPC of linear systems in state space form

## Slide 18: MPC Controller
Open Loop solution
𝑥(𝑘+𝑖)=𝐴^𝑖 𝑥(𝑘)+∑24_(𝑗=0)^(𝑖−1)▒𝐴^(𝑖−𝑗−1) 𝐵𝑢(𝑘+𝑗), 𝑖>0
, , ,
𝑋(𝑘)=[■8(𝑥(𝑘+1)@𝑥(𝑘+2)@⋮@𝑥(𝑘+𝑁−1)@𝑥(𝑘+𝑁))], 𝒜=[■8(𝐴@𝐴^2@⋮@𝐴^(𝑁−1)@𝐴^𝑁 )], 𝑈(𝑘)=[■8(𝑢(𝑘)@𝑢(𝑘+1)@⋮@𝑢(𝑘+𝑁−2)@𝑢(𝑘+𝑁−1))], ℬ=[■8(𝐵&0&⋯&0&0@𝐴𝐵&𝐵&⋯&0&0@⋮&⋮&⋱&⋮&⋮@𝐴^(𝑁−2) 𝐵&𝐴^(𝑁−3) 𝐵&…&𝐵&0@𝐴^(𝑁−1) 𝐵&𝐴^(𝑁−2) 𝐵&…&𝐴𝐵&𝐵)]
Open Loop solution

## Slide 19: MPC Controller
Open Loop solution
𝑋(𝑘)=𝒜𝑥(𝑘)+ℬ𝑈(𝑘)
𝒬=[■8(𝑄&0&⋯&0&0@0&𝑄&⋯&0&0@⋮&⋮&⋱&⋮&⋮@0&0&⋯&𝑄&0@0&0&…&0&𝑆)], ℛ=[■8(𝑅&0&⋯&0&0@0&𝑅&⋯&0&0@⋮&⋮&⋱&⋮&⋮@0&0&⋯&𝑅&0@0&0&…&0&𝑅)]
𝑎𝑟𝑔{min_(𝑢(.))⁡〖𝐽(𝑥(𝑘),𝑢(.),𝑘)〗 }=𝑎𝑟𝑔{min_(𝑈(𝑘))⁡〖𝐽 ̅(𝑥(𝑘),𝑈(𝑘),𝑘)〗 }
𝐽 ̅(𝑥(𝑘),𝑈(𝑘),𝑘)=𝑋^′ (𝑘)𝒬𝑋(𝑘)+𝑈′(𝑘)ℛ𝑈(𝑘)
Open Loop solution

## Slide 20: MPC Controller
Quadprog in Matlab
𝐻=ℬ^′ 𝒬ℬ+ℛ
Matlab function:
𝐹=𝒜′𝒬ℬ
Quadprog in Matlab
Notes: 𝑙𝑏=−0,262 𝑟𝑎𝑑; 𝑢𝑏=0,262 𝑟𝑎𝑑

## Slide 21: MPC without info on control constraints
MPC without info in control constraints (Q_d, R_d=)
MPC without info in control constraints (Q_d=𝑄_4, R_d=𝑅_4)

## Slide 22: MPC without info on control constraints
Results for MPC without info on control constraints

## Slide 23: MPC with info on control constraints
MPC with info on control constraints (Q_d, R_d=)
MPC with info on control constraints (Q_d=𝑄_4, R_d=𝑅_4)
Notes: PUNTO 4

## Slide 24: MPC with info on control constraints
Results for MPC with info on control constraints

## Slide 25: MPC with constraints
MPC with constraints (Q_d, R_d=)
MPC with constraints (Q_d=𝑄_4, R_d=𝑅_4)

## Slide 26: MPC with constraints on pitch angle state : x2
Implementation
Notes: PUNTO 5

## Slide 27: MPC with constraints on pitch angle state : x2
Implementation

## Slide 28: MPC with constraints on pitch angle state : x2
SETTINGS:
Pitch angle <= (+/-) 20°
Blue: pitch angle costrained
Red: without pitch angle costraint
<= 0,262 rad

## Slide 29: MPC with overshot constraint on altitude state : x2
X4 comparison: with set costrain (red) we have a much slower system on x4 but we can reduce the overshot

## Slide 30: MPC with overshot constraint on altitude state : x4
Implementation

## Slide 31: MPC with overshot constraint on altitude state : x4
SETTINGS
Overshot set: 0;
Altitude comparison zoomed: with set costrain (green) we have no overshot
Historical mpc comparison since LQ

## Slide 32: MPC with overshot constraint on altitude state : x4
X2 comparison: with set costrain (black) we have slightly worst performance but x2 constrain remains satisfied

## Slide 33: MPC with slew rate costraint on input
|

## Slide 34: MPC with slew rate costrain on input
SETTINGS:
U comparison with slew rate costraint

## Slide 35: MPC with slew rate costrain on input
With slew rate constraint, the state x4 is not altered

## Slide 36
Kalman filter
Optimal observer
State estimation since states measurements are not available
]
Notes: POINT 8

## Slide 37
Kalman filter: state comparison

## Slide 38: MPC with Control Constraints
Control Constraints
𝑢_𝑚𝑖𝑛≤𝑢(𝑘)≤𝑢_𝑚𝑎𝑥 ∀𝑘
𝐴_𝑢 𝑢(𝑘)≤𝑏_𝑢 ∀𝑘∈[0;𝑁−1]
𝐴 ̂_𝑢=[■8(𝐴_𝑢&0&⋯&0@0&𝐴_𝑢&⋯&0@⋮&⋮&⋱&⋮@0&0&⋯&𝐴_𝑢 )], 𝑏 ̂_𝑢=[■8(𝑏_𝑢@𝑏_𝑢@⋮@𝑏_𝑢 )]
𝐴 ̂_𝑢 𝑈(𝑘)≤𝑏 ̂_𝑢
Control Constraints
States Constraints
𝐴_𝑥 𝑥(𝑘)≤𝑏_𝑘 ∀𝑘∈[1;𝑁]
𝐴 ̂_𝑥=[■8(𝐴_𝑥&0&⋯&0@0&𝐴_𝑥&⋯&0@⋮&⋮&⋱&⋮@0&0&⋯&𝐴_𝑥 )], 𝑏 ̂_𝑥=[■8(𝑏_𝑥@𝑏_𝑥@⋮@𝑏_𝑥 )]
𝐴 ̂_𝑥 𝑋(𝑘)≤𝑏 ̂_𝑥↔𝐴 ̂_𝑥 (𝒜𝑥(𝑘)+ℬ𝑈(𝑘))≤𝑏 ̂_𝑥
𝑥_𝑚𝑖𝑛≤𝑥(𝑘)≤𝑥_𝑚𝑎𝑥 ∀𝑘≥0
States Constraints

## Slide 39: MPC with Control Constraints
,
𝐴 ̂=[■8(𝐴 ̂_𝑥 ℬ@𝐴 ̂_𝑢 )], 𝑏 ̂=[■8(𝑏 ̂_𝑥−𝐴 ̂_𝑥 𝒜𝑥(𝑘)@𝑏 ̂_𝑢 )]
𝐴 ̂𝑈(𝑘)≤𝑏 ̂
Control Constraints States Constraints
Control Constraints States Constraints

## Slide 40: Displacement diagrams
Modified trapezoidal

## Slide 41: Motion Curve 01: Feeding Group
0° → 80° Rise
80° → 360° Dwell

## Slide 42: Motion Curve 02: Pressing Group
0°→90° Ground
90°→135° Rise
135°→305° Dwell
305°→350° Fall
350°→360° Ground

## Slide 43: Motion Curve 03: Cutting Group
0°→145° Ground
145°→220° Rise
220°→295° Fall
295°→360° Ground

## Slide 44: Cutting group
Crank slider continuous
Crank slider go and return
Ball screw

## Slide 45: Crank slider continuous
Connecting rod (b) 150 mm
Crank (a) 50 mm
Chart: 
| cutting rising | cutting falling | other motion curves
Vendite | 40 | 40 | 280

## Slide 46: Kinematics and dynamics Crank slider continuous
Notes: Cut resistance 15000N same independent from the section of the wire

## Slide 47: Crank slider go and return
Connecting rod (b) 150 mm
Crank (a) 50 mm
Inverse
kinematics
Power balance

## Slide 48: Kinematics and dynamics Crank slider go and return

## Slide 49: Ball screw
Pitch of the screw (p) 2 mm
Trapezoidal screw M20 R = 10 mm
Inverse
kinematics

## Slide 50: Kinematics and dynamics Ball screw

## Slide 51: Motor-reducer sizing: ball screw (alpha and beta procedure)
Chosen
Motor 5
Reducer 6

## Slide 52: Motor-reducer sizing: crank slider go and return (alpha and beta procedure)
Chosen
Motor 11
Reducer 2

## Slide 53: Motor-reducer sizing: Crank slider continuous (static dimensioning)
Chosen
Motor 1
Reducer 8

## Slide 54: Performance analysis
Different cutting length

## Slide 55: Performance analysis
Comparison of motor weights
name | BLS-115 | BLS-191 | BLS-144
[kg] |  |  | 20.1
name | BLS-115 | BLS-191 | BLS-144
[kg] |  |  | 20.1

## Slide 56: Possible improvements
Inverse
kinematics

## Slide 57: Thank you for your attention!
Crippa Davide 509769
Moroni Gianluca 503424
Mongini Paolo 507997